## Slide 1: FP98 SQUIDS and Noise Thermometers
Coc, Q’ inich & Huth, Paris
Experiment perfomed the 21.11.2024
Tutor: Brunold, Axel

## Slide 2
Goals of the experiment
Theoretical Background
  Super conductivity
  SQUIDs
  Noise thermometers
Measuring principles
  dc-SQUID Characteristics
  FLL mode
  Two-stage SQUID Readout
Experiment Setup & Tasks
Evaluation of measurements
Discussion & Comments
  Result’s Overview
  Discussion
  Comments
Structure

## Slide 3
1. Goals of experiment
  Learn the basics of low-temperature physics and superconductivity
  Learn the basics of SQUIDs and noise thermometers
  Learn how to operate dc-SQUIDs

## Slide 4: 2. Theoretical background

## Slide 5
  2.1. Superconductivity
  Resistance vanishes below a critical temperature TC
    When the critical current IC or critical flux density BC is exceeded, enters a normal state.
  Not equivalent to an ideal conductor
    Expulsion of the magnetic field below critical temperature
  Type I
    Either in a superconductive or normal state
    Perfect Diamagnets up to critical Field HC
  Type II
    Additional mixed-state producing magnetic field vortexes
2. Theoretical background
Fig. 1: Meißner Ochsenfeld effect
Notes: superconducting coherence length ξ in addition to London magnetic field penetration depth λ. According to Ginzburg–Landau theory, in a type-II superconductor λ/ξ>1/2.
Each vortex obeys London's magnetic flux quantization and carries one quantum of magnetic flux Φ0.
Magnetic flux density B
Magnetic Field H

## Slide 6
  2.1. Superconductivity
  2.1.2. Flux Quantization
  Consider closed loop of superconducting material
  and
  Inside the ring (London penetration depth)
  Superconducting currents on the surface
  Phase difference of
  Enclosed magnetic flux
  Screening currents maintain trapped flux
2. Theoretical background
Notes: B field, magnetic flux density going through the ring (top picture)
H penetrates into volume -> magnetization. Supercurrents on the surface which don’t decay in time. B-> 0, the B-field inside the loop gets trapped.

## Slide 7
  2.1. Superconductivity
  2.1.1. Cooper-pairs (CPs)
  Attractive interaction between electrons due to interaction with atom lattice
  CP described by a two-particle wave function
  CP behave like bosons
   CPs condensate, i.e. common macroscopic ground-state wave-function
2. Theoretical background
Notes: Spins of two electrons couple to the singlet state S=0 Flux quantization and Josephon-effect are caused by the common macroscopic wave-funciton

## Slide 8
  2.1. Superconductivity
  2.1.3. Josephson Junction
  Consider two superconductors separated by thin insulator
  and are coupled
  dc Josephson effect : phase difference dependent (dc-)current. Critical current
  ac Josephson effect: for causing (ac-current).
  For critical currents depend on
  If externally applied other contributions to total current: &
2. Theoretical background
Notes: n_i = density of cooper pairs if both S_i are from same material n_1 = n_2
Chemical potential equal for zero V, kappa coupling constant
Phase of CPs
Omega_j = josephson frequency
Supercurrent I_S: Flowing without a voltage with dc JE | Zero voltage state
ac JE | Voltage state

## Slide 9
  2.1. Superconductivity
  2.1.3. Josephson Junction
  : Normal current
  Thermal and electrical energy break CPs. Broken CPs tunnel through the gap
  Obeys Ohm’s law with resistance
  for
  : Fluctuation current
  Brownian motion of quasiparticles creates current noise
  Nyquist’s theorem
2. Theoretical background
Notes: For T>0 thermal energy breaks CPs
I> I_C aka V = I*R> V_g electric. Breaks CPs

## Slide 10: 3. Measuring principles

## Slide 11
  3.2. Noise thermometers
  3.2.1. Thermal noise
  Brownian motion of electrons within a conductor
  Nyquist formula
  : Temperature; resistance; bandwidth
  Thermometers with wide measuring range
  Measure the thermal noise of electrons
  Challenges: for
  Amplification device with low intrinsic noise is required
  Solution: SQUIDs
3. Measuring principles
3. Measuring principles
Notes: Brownian motion: random movement of particles in a liquid medium due to thermal movement of medium and particles
Proportion between varian and T,R, \Delta f found, Nyquist identified it as thermal motion

## Slide 12
  3.2. Noise thermometers
  3.2.2. Spectral functions/density
  Every dissipative component is (in general) frequency-dependent
  Fourier transform of measured signals
  Often square root spectral density is considered
  ;
3. Measuring principles
3. Measuring principles
Notes: <A^2> = \int_f_0^f_0+\Deltaf insert niquist formula and derivate i.r f
S_I user kirschhoff’s low

## Slide 13
  3.2. Noise thermometers
  3.2.2. Spectral functions/density
3. Measuring principles
Notes: <A^2> = \int_f_0^f_0+\Deltaf insert niquist formula and derivate i.r f
S_I user kirschhoff’s low

## Slide 14
  3.3. SQUIDs
  Direct-current Superconducting Quantum Interference Device (dc-SQUID)
  Superconducting loop with 2 (or 1) Josephson Junctions -> dc(rc)-SQUID
  Super current : tunneling of CPs
  Shielding Factor with shielding current
  Flux in SQUID sensible to external flux
   Sensitive magnetometers
3. Measuring principles

## Slide 15
  3.3.1. dc-SQUID Characteristics
  Non-ideal junctions
  Constant bias current
      : no dissipation voltage drop
  depends periodically on the trapped magnetic flux
    Voltage drop
  Superconducting coil causes changes in flux
  Optimal parameters: Iw_B with highest voltage drop and Φ at inflection point of Φ-V characteristic
  No yet a magnetometer: is periodic
3. Measuring principles
Notes: Coil couples to super conducting ring
I_\Phi current through coil , M: mutual inductance

## Slide 16
  3.3.1. dc-SQUID Characteristics
3. Measuring principles
Notes: <A^2> = \int_f_0^f_0+\Deltaf insert niquist formula and derivate i.r f
S_I user kirschhoff’s low

## Slide 17
  3.3.2. Flux-Locked-Loop
  Goal: linearize output signal
  Negative flux feedback using via
  feedback coil and
  Feedback causes flux change until the voltage
  drop over SQUID is zero
  with
  Workingpoint  optimal: strong dependence
  Magnetometer: measure flux changes produced by
3. Measuring principles
Notes: Workingpoint, set of parameters in which the system is stable: remains the same for different perturbations, aka. Input signals

## Slide 18
  3.3.3. Two-stage SQUID-Readout
  Increase of signal to noise ratio
  Second-stage SQUID: array of SQUIDS
  ampflified by two stages before integration and feedback
  Frontend:
  Flux change in first stage generates current change  Flux change in second SQUID
  Workingpoint (, , ,
3. Measuring principles
Notes: Figure: two-stage FLL SQUID
Flux change in the first SQUID generates flux change in \Delata\Phi_2 input coil

## Slide 19: 4. Experiment setup & tasks

## Slide 20
  4.1. Set up
4. Experiment setup & tasks

## Slide 21
  4.2. Tasks
  Single-stage SQUID: Open-loop mode
  Measure characteristics
    Estimate and .
  Measure characteristics
    Determine the inverse mutual inductance and .
  Single-stage SQUID: FLL mode
  Measure resulting from periodic triangular input signal
      Determine amplification factor
  Measure spectrum in FLL mode varying GBP
      Find optimal value for GBP
4. Experiment setup & tasks

## Slide 22
  4.2. Tasks
  Temperature measurement :
  Using a double-stage SQUID
  Measure characteristic in open loop mode
      Find optimal working point
  Measure the noise spectrum
    Measure the temperature of liquid
4. Experiment setup & tasks

## Slide 23: 5. Evaluation of measurements

## Slide 24
  5.1. Single-stage SQUID
  5.1.1. Open-loop
  Measure characteristic
  All parameters set to zero
  Vary input signal
  ideal value = biggest voltage
5. Evaluation of measurements
input-signal
Notes: Set everyting to zero. Only turn on biasing current. AMP mode (open loop) U_out amplified by 2000

## Slide 25
Fig. 1.1: Measured and of a single-stage SQUID in open-loop mode with bias current A.
  5.1. Single-stage SQUID
  5.1.1. Open-loop
  Measure characteristic
5. Evaluation of measurements
Fig. 1.2: Measured and of a single-stage SQUID in open-loop mode with optimal bias current A.
Notes: Set everyting to zero. Only turn on biasing current. AMP mode (open loop) U_out amplified by 2000

## Slide 26
  5.1. Single-stage SQUID
  5.1.1. Open-loop
  Measure characteristic
  Transform the measured voltage into current
  and
  Use Ohm’s law to get resistance
  Consider offset by adding
  Take into consideration the amplification factor of output signal
5. Evaluation of measurements

## Slide 27
  5.1. Single-stage SQUID
  5.1.1. Open-loop
  Measure characteristic
5. Evaluation of measurements
Fig. 2: characteristic of a single-stage SQUID (right) and linear fit to its linear range (left)

## Slide 28
  5.1. Single-stage SQUID
  5.1.1. Open-loop
  ii. Measure characteristic
  Signal through respective coil
  Search for ideal
  Use to center output signal
  Around 0
5. Evaluation of measurements
input-signal
bias current
bias voltage
Notes: Set everyting to zero. Only turn on biasing current. AMP mode (open loop) U_out amplified by 2000

## Slide 29
  5.1. Single-stage SQUID
  5.1.1. Open-loop
  ii. Measure characteristic
5. Evaluation of measurements
Fig. 3: Measured and (left), and and (right) of a single-stage SQUID. Optimal parameters: A and A
Notes: Turn on function input-signal in repective coil. Bias current I_B: maximal U_out swing. U_B center U_out around zero
Problem: multiple values with same voltage swing

## Slide 30
  5.1. Single-stage SQUID
  5.1.1. Open-loop
  ii. Measure characteristic
  Transform measured into (analoge to previous measurement)
  Consider amplification factor of
  Tranform x-axis , time required for signal to reach next maxima
  Consider transformation of functions:
  Use  linear fit for curve
5. Evaluation of measurements

## Slide 31
  5.1. Single-stage SQUID
  5.1.1. Open-loop
  ii. Measure characteristic
5. Evaluation of measurements
Fig. 4: (left) and (right) characteristic
Fig. 5: (left) and (right) characteristic with linear fit to

## Slide 32
  5.1. Single-stage SQUID
  5.1.2. FLL mode
  i. Measure resulting from periodic triangular input signal
  Input-signal
  Find optimal bias current
  Use to center output signal around 0
  We find:
  A V.
5. Evaluation of measurements
input-signal
bias current
bias voltage
Notes: Generator in I_\Phi_B, M_\Phi_B is M_IN. I_B maximal voltage swing. Turn off genetarot I_Phi_B to move U_out to zero. Singal to Phi_X move U_out to zero.

## Slide 33
  5.1. Single-stage SQUID
  5.1.2. FLL mode
  i. Measure resulting from periodic triangular input signal
  Input-signal
  Keeping optimal and
  Use to center output signal around
  We find:
5. Evaluation of measurements
input-signal
bias current
Notes: Generator in I_\Phi_B, M_\Phi_B is M_IN. I_B maximal voltage swing. Turn off genetarot I_Phi_B to move U_out to zero. Singal to Phi_X move U_out to zero.

## Slide 34
  5.1. Single-stage SQUID
  5.1.2. FLL mode
  i. Measure resulting from periodic triangular input signal
5. Evaluation of measurements
Fig. 5: Measured and of a single-stage SQUID in FLL mode. Workingpoint:
Notes: Generator in I_\Phi_B, M_\Phi_B is M_IN. I_B maximal voltage swing. Turn off genetarot I_Phi_B to move U_out to zero. Singal to Phi_X move U_out to zero.

## Slide 35
  5.1. Single-stage SQUID
  5.1.2. FLL mode
  i. Measure resulting from periodic triangular input signal
  Transform into
  Fit linear function to curve
5. Evaluation of measurements

## Slide 36
  5.1. Single-stage SQUID
  5.1.2. FLL mode
  i. Measure resulting from periodic triangular input signal in FLL mode
5. Evaluation of measurements
Fig. 6: Measured and signals (left) and linear fit to the curve (right)

## Slide 37
  5.1. Single-stage SQUID
  5.1.2. FLL mode
  Measure resulting from periodic triangular input signal
  Calculate amplification factor using previously calculated variables
  
  We find :
  V
  Comparison between both values:
5. Evaluation of measurements

## Slide 38
  5.1. Single-stage SQUID
  5.1.2. FLL mode
  ii. Measure noise spectrum
  Validity range: GBP where
  no resonances are formed.
   GBP must be smaller than
  16GHz
5. Evaluation of measurements
Fig. 7: Measured noise spectrum in FLL mode at GBP = 3.3 GHz with workingpoint parameters

## Slide 39
  5.2. Temperature measurement
  i. Measure characteristic in open-loop mode
  First: Tune SQUID array
  as a single-stage SQUID
  Input-signal
  Find optimal bias current
  Use to center output signal around
  We find:
  A V
5. Evaluation of measurements
input-signal
bias current
Bias voltage
Notes: First Tunne array like 1-s. SQUID. Signal I_Phi_X find I_B. Center U_out around 0 with U_B. While array is optimal. Turn on signal I_\Phi_B find bias of frontend SQUID I . Center with I_\Phi_X

## Slide 40
  5.2. Temperature measurement
  i. Measure characteristic in open-loop mode
  Second: Tune frontend SQUID
  Keep optimal values of second-stage
  SQUID
  Input-signal
  Find optimal bias current
  Use to center output signal
  around
  We find:
  A A
5. Evaluation of measurements
bias current
bias current
input-signal
Notes: First Tunne array like 1-s. SQUID. Signal I_Phi_X find I_B. Center U_out around 0 with U_B. While array is optimal. Turn on signal I_\Phi_B find bias of frontend SQUID I . Center with I_\Phi_X

## Slide 41
  5.2. Temperature measurement
  i. Measure characteristic in open-loop mode
5. Evaluation of measurements
Fig. 8: characteristic at optimal working point (, , ,
Notes: First Tunne array like 1-s. SQUID. Signal I_Phi_X find I_B. Center U_out around 0 with U_B. While array is optimal. Turn on signal I_\Phi_B find bias of frontend SQUID I . Center with I_\Phi_X

## Slide 42
  5.2. Temperature measurement
  ii. Measure noise spectrum in FLL mode
  Turn off function generator
  Keep previously found optimal
  parameters
  Use to center signal around zero
  We find:
  A
  Stable working point for temperature
  measurement
5. Evaluation of measurements
Bias-current
Notes: First Tunne array like 1-s. SQUID. Signal I_Phi_X find I_B. Center U_out around 0 with U_B. While array is optimal. Turn on signal I_\Phi_B find bias of frontend SQUID I . Center with I_\Phi_X

## Slide 43
  5.2. Temperature measurement
  ii. Measure noise spectrum in FLL mode
5. Evaluation of measurements
Fig. 9: Measured noise spectrum in FLL mode at optimal working point.
Notes: Turn off all input signals and

## Slide 44
  5.2. Temperature measurement
  ii. Measure noise spectrum in FLL mode
  Transform measured spectrum into voltage spectral density
  
  Transform voltage spectral density into current spectral density
  
  Fit expected current spectral density to measured and
  
5. Evaluation of measurements

## Slide 45
  5.2. Temperature measurement
  ii. Measure noise spectrum in FLL mode
5. Evaluation of measurements
Fig. 10: Measured current density function (blue line) and fitted model (green line)
Notes: Mention what motivates the fitting-range

## Slide 46: 6. Discussion & Comments

## Slide 47
  6.2. Discussion
Single-stage SQUID’s characteristics consistent with flux-quantization
Linearization of signal in FLL mode
Measured consistent with literature
6. Discussion & Comments

## Slide 48
  6.2. Discussion
(Small) fit parameters’ errors are not representative
 Use more than one period of input signal for parameter estimation
off. Expected A
Inadecuate tuning: voltage drop constant for an interval of applied current
Significant deviation between and
 Missing statistical and systematic errors
 Problems from estimation
Tuning of double-stage SQUID is not ideal
Fine tuning
A larger fit range of could improve the precision of
6. Discussion & Comments

## Slide 49
  6.3. Comments
  Pros:
  Done in one evening
  Easy operation
  Cons:
  PEPV not indispensable, but helps with understanding
  Electronics can feel abstract
  Lab’s script not ideal
    Nomenclature
    Evaluation
  Recommendation:
  Careful reading of tasks
5. Discussion & Comments